## Slide 1: Welcome!
Electrical Training Week 2

## Slide 2: Last Week!
What are Microcontrollers?
Intro to C++
Prototyping

## Slide 3: This Week!
Introduction to PCBs
Introduction to KiCad
Parts and Libraries in KiCad
Configuring KiCad Setup
Making a Part in KiCad

## Slide 4: What are PCBs?

## Slide 5: Printed Circuit Boards (PCBs)
A way to construct more electrically complex circuits that are impractical for a breadboard
Have a wide range of components (sensors, MCUs, power circuit components) that are often surface mount (SMD) rather than through hole
Through Hole
Surface Mount
Notes: Week 1 was focused on doing design with a breadboard and wires to make electrical components. With more components this gets too complicated
Shift then to focus on PCBs which have the same range of components we have worked with earlier but we are able to make connections through copper traces on a 2D level
PCBs take advantage of SMD which are smaller to create more efficient designs

## Slide 6: Layers
Work by having multiple different layers
Silkscreen - Text, labels, and graphics
Soldermask - repels solder, usually colored green
Copper - conductive materials
Substrate - for structure
Notes: Instead of using wires and a breadboard we now have multiple layers of material on a 2D place
Silkscreen for text (for us usually white) that will help us with soldering
Soldermask aka the green stuff that doesnt get soldered
Copper actually makes the electrical connections throught traces and vias
Substrate provides structure

## Slide 7: PCB Features
Training Board
Notes: The PCB you will be interacting with the next couple of days and edit the design of
Some notable features are pointed out
SMD component - can see copper pads to solder too
Through hole component, can see holes
Copper traces for connections
Silkscreen for label

## Slide 8: Team Examples
We use PCBs for a wide range of problems
Notes: RW Control Board
RC Kicker Board
RR PoE
IGVC Logic Board

## Slide 9: What is KiCad?
Where the magic happens

## Slide 10: KiCad
Computer software to design PCBs
Three Stages of Development
  Libraries & Parts
  Schematics
  Board Layout
Notes: Libraries - Store the components that you will include on your board
Schematics - Defines circuits between all the components you have included
Board Layout - Defines the physical location of components and their physical connections

## Slide 11: Control Panel
Notes: Navigation window for EAGLE
Can access recent files, open files, make new files
On the right side I have shown my libraries which are designated with the book shaped icon

## Slide 12: Libraries
Store various components used in projects
Libraries organize devices (electrical components) to be comprised of a symbol and footprint

## Slide 13: Symbol
Used in the schematic view to make circuit connections with other component symbols

## Slide 14: Footprint
Used in the the board layout view to make the actual physical connections between components

## Slide 15: Common Packages
Many parts utilize industry standardized footprints so many different parts can have the same footprint
Notes: Packages can be “copied and pasted” in EAGLE once you know the package your component comes in.

## Slide 16: Device
Links the symbol and footprint together by mapping the symbol’s pins to the footprint pins
A symbol can have multiple footprints if the component comes in multiple different packages (common with ICs)

## Slide 17: Example Library

## Slide 18: Example Library
A component with multiple footprints

## Slide 19: Lab!
Setup + Making a Part in KiCad

## Slide 20: Installing Software
EAGLE
  Requires Autodesk account registered with GT email (click “Get Started”)
    https://www.autodesk.com/education/edu-software/overview
  Download here
    https://www.autodesk.com/products/eagle/free-download

## Slide 21: Adding Repositories
Adding the #eagle-libraries repository where RJ parts are stored
You will be using Github Desktop for this
  https://desktop.github.com

## Slide 22: Making a Part - Symbol
Based on pin configuration in the datasheet create similarly named pins and create an outline

## Slide 23: Making a Part - Footprint
Create a physical representation of the the part by reading the package outline details in the datasheet and then placing correctly sized pads/drills at the appropriate location

## Slide 24: Making a Part - Device
Map the symbol’s pins to the footprint’s pads, add prefix, and add descriptive information

## Slide 25: Thank You!
Any Questions?