## Slide 1: Welcome
Soldering Training 2023

## Slide 2: Agenda
Introduction
Board overview - what are we soldering?
How to Solder
  Basics
  Tools
  Component Types
Soldering Instructions
Debugging

## Slide 3: Introduction
What is RoboJackets?

## Slide 5: RoboJackets Electrical
Embedded System Design
  Printed Circuit Board design
    Analog and Digital Circuitry
  Microcontroller firmware programming
  Control systems
A bunch of other cool stuff!

## Slide 6: Training Board Overview

## Slide 7: The Board

## Slide 8: Purpose
Control a brushed DC motors using an Arduino Uno
  Motor Driver chips controlled with logic/PWM signals from Arduino
Source power from 12V DC Barrel Jack

## Slide 9: Components
DC Barrel Jack
  Source power
Screw Terminal
  To attach motor wires
Power Switch
  Turn motor on or off
Fuse
  Overcurrent protection

## Slide 10: Components
Reset Button
  Reboots Microcontroller
Motor Driver
  Converts logic signals to motor power
Indication LEDs
  Visually indicate power, fuse, and status of system

## Slide 11: Soldering
I suppose this is what you actually came here for...

## Slide 12: Safety
Hold like a pencil from plastic grip area
Entire metal gets hot (not just the tip!)
Make sure iron is in holder when not in use

## Slide 13: Supplies
Solder Metal that is melted to form joints
Solder Metal that is melted to form joints
Sponge For cleaning iron tip
Flux Helps solder to flow more easily

## Slide 14: Supplies
Iron Tips - Choose based on desired precision and heat transfer capability

## Slide 15: Supplies
Exhaust Fan
  Keep solder fumes out of your lungs
Desoldering Wick
  Copper mesh to remove solder
Desoldering Pump
  Sucks out undesired solder

## Slide 16: Through-Hole Soldering
Place pins in hole
Touch iron to both pin and pad simultaneously
Apply solder to pad at opposite side of iron
Remove solder, then iron, then clip excess

## Slide 17: Heating Technique
Touch both the component and the pad at the same time
Make sure to apply solder to the pad, not the iron
  Remove solder before removing iron

## Slide 18: How much Solder?
Fully cover the pad, but don’t form a bubble

## Slide 19: Surface Mount Components
Wet one pad with Solder
Place component on pad and remove iron
Solder remaining pads before reflowing first pad

## Slide 20: Other Soldering Techniques/Tips

## Slide 21: Hot Air Gun

## Slide 22: Solder Paste

## Slide 23: Reflow Oven

## Slide 24: Soldering Stencil
Apply paste using stencil
Remove stencil and place all components
Place circuit board in reflow oven

## Slide 25: Tips
Previously mentioned techniques heat up entire circuit board
Some components cannot stand the heat
  Make sure your components (especially connectors) can take the heat

## Slide 26: LED Direction
“Arrow points towards the house”
The “house” side is the cathode side which should be on the same side as the marking on the solder mask

## Slide 27: Pin Direction

## Slide 28: Soldering Activity!
Solder the training board

## Slide 29: Sample Board

## Slide 30: Debugging
Complex boards rarely work first time

## Slide 31: Questions to Ask
What is the expected behavior?
What is the current behavior?

## Slide 32: Getting Started
Top-Down Methodology

## Slide 33: Done Soldering?
Always check for shorts!
Is there an oopsie?

## Slide 34: Is the power bus active?
Power LEDs can save tons of time here
But were they soldered correctly?
Continuity/Diode Mode

## Slide 35: “Hello World”
Test basic code first

## Slide 36: Every Circuit is Different
Always start general to not waste time
A few more pointers:
Data not being sent correctly?
  Continuity between end points
  Continuity to adjacent lines
  Is firmware using the correct pins?
  Could try reflowing the data lines or associated devices
Useful debugging tools
  Multimeter
    Voltage check
    Continuity check
  Oscilloscope
    Can see waveforms over time
      Useful to analyze noise issues
    Many have decoding features
      Isolate problems to transmitter or receiver ends

## Slide 37: Debugging Activity
Sorry not sorry